## Slide 1: Advanced Robotics Programming Class Lesson 3: Creating a Robot Base with TeleOp Control
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn:
  Simple Motor
  Simple Servo
  Enhanced Servo
  Game Controller and Button Panel
  Control a motor using analog joystick
  Control a servo using game controller button
  Control a simple drive base using analog joystick
  Student exercise: Create a mecanum drive base and control it with analog joystick

## Slide 3: Simple Motor
Create an instance of a motor controller object (e.g. FrcCANTalon).
Motor controller object properties:
  Motor direction.
  Encoder direction.
  Encoder and odometry.
  Limit switches.
  Reset odometry on digital trigger.
  Zero calibration.
  Brake mode.
  Power mode vs velocity mode.
  Built-in PID control.

## Slide 4: Simple Servo
Create an instance of a servo object (TrcServo).
Servo object properties:
  Servo direction.
  Servo position.
  Logical position vs Physical position.

## Slide 5: Enhanced Servo
Create an instance of an enhanced servo object (TrcEnhancedServo).
Enhanced servo object properties:
  Dual servo support.
  Regular servo vs continuous servo.
  Limit switches support.
  Encoder support.
  Range calibration.
  Speed control and step mode.

## Slide 6: Game Controller and Button Panel
Create an instance of a game controller object.
Typical game controller consists of:
  A number of analog sticks (can have multiple axes).
  A number of analog throttles/twists.
  A number of buttons.
Button panel consists of an array of buttons.
Game controller/Button panel object properties:
  Y axis direction.
  Analog control deadband.
  Analog control response curve.
  Button event handler.

## Slide 7: Control a Motor with Analog Joystick
Create and configure a game controller.
Create and configure a motor.
Enable motor odometry.
Add code to read joystick value and set motor power with it.
Add code to display motor odometry.

## Slide 8: Control a Servo with Game Controller Buttons
Create and configure a game controller.
Create and configure a servo.
Create a button event handler and hook it up to the game controller object.
Add code to the button event handler to set servo positions responding to button events.

## Slide 9: Control a Simple Drive Base with Analog Joysticks
Create left and right wheel motors.
Configure wheel motors.
Enable motor odometry.
Create a Simple Drive Base with the wheel motors.
Configure drive base.
Enable drive base odometry.
Add code to read joystick values and set drive base power with it.
Add code to display drive base odometry.

## Slide 10: Student Exercise
Create and control a mecanum drive base with analog joysticks.
  …