## Slide 1: Advanced Robotics Programming Class Lesson 3: Creating a Robot Base with TeleOp Control
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn:
  Simple Motor
  Game Controller and Button Panel
  Control a Motor With Analog Joystick
  Student Exercise: Create a simple drive base and control it with analog joystick
  Student exercise: Create a mecanum drive base and control it with analog joystick

## Slide 3: Simple Motor
Two types of motor controllers: simple motor controllers, smart motor controllers (PWM vs. communication protocol).
Create an instance of a motor controller object.
Example: FrcCANTalon – Constructor needs instance name and CAN ID.
Motor controller object properties:
  Motor direction.
  Encoder direction.
  Encoder and odometry.
  Limit switches.
  Reset odometry on digital trigger.
  Zero calibration.
  Brake mode.
  Power mode vs velocity mode.
  Built-in PID control.

## Slide 4: Game Controller and Button Panel
Create an instance of a game controller object.
Example: FrcJoystick, FrcXboxController – Constructor needs instance name and port number.
Typical game controller consists of:
  A number of analog sticks (can have multiple axes).
  A number of analog throttles/twists.
  A number of buttons.
Button panel consists of an array of buttons.
Game controller/Button panel object properties:
  Y axis direction.
  Analog control deadband.
  Analog control response curve.
  Button event handler.

## Slide 5: Control a Motor with Analog Joystick
Understanding analog joystick input to power output curve.
Create and configure a game controller.
Create and configure a motor.
Enable motor odometry.
Add code to read joystick value and set motor power with it.
Add code to display motor odometry.
Chart: Power Output vs Joystick Input

## Slide 6: Exercise: Simple Drive Base
Control a simple drive base with analog joysticks.
  Create and configure game controller(s).
  Create and configure 2 motors.
  Create and configure a simple drive base with the 2 motors.
  Add TeleOp code to run the simple drive base with the joysticks using tank drive.
  Enable motor and drive base odometries.
  Add code to display drive base odometry.

## Slide 7: Exercise: Mecanum Drive Base
Control a mecanum drive base with analog joysticks.
  Create and configure game controller(s).
  Create and configure 4 motors.
  Create and configure a mecanum drive base with the 4 motors.
  Add TeleOp code to run the mecanum drive base with the joysticks.
  Enable motor and drive base odometries.
  Add code to display drive base odometry.