## Slide 1: Advanced Robotics Programming Class Lesson 4: Robot Subsystems
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn:
  Simple Servo
  Enhanced Servo
  Student Exercise: Control a servo using game controller button
  Pneumatic
  Student Exercise: Control pneumatic using buttons on a button panel
  PID Controlled Actuators (e.g. Elevator)
  Student Exercise: Control an elevator using a joystick

## Slide 3: Simple Servo
Create an instance of a servo object.
FrcServo: Constructor needs instance name and a PWM channel number.
Servo object properties:
  Servo direction.
  Servo position.
  Logical position vs Physical position.

## Slide 4: Enhanced Servo
Create an instance of an enhanced servo object.
TrcEnhancedServo – Constructor needs instance name, one or two physical servos, optional lower/upper limit switches.
Enhanced servo object properties:
  Dual servo support.
  Regular servo vs continuous servo.
  Limit switches support.
  Encoder support.
  Range calibration.
  Speed control and step mode.

## Slide 5: Exercise: Simple Servo
Control a simple servo using buttons on a button panel.
  Create and configure a game controller.
  Create and configure a servo.
  Create a button event handler and hook it up to the game controller object.
  Add code to the button event handler to set servo positions responding to button events.
  Add code to display servo status.

## Slide 6: Pneumatic
Create an instance of a pneumatic object.
FrcPneumatic – Constructor needs PCM number and one or more channel numbers.
Pneumatic object properties:
  Set pneumatic channels ON or OFF.
  Set pneumatic channels ON only for the specified period.
  Set pneumatic channel pattern 1 for set period 1 and then pattern 2 for set period 2 and optionally repeat.
  Set action list that specifies what channel pattern to set for the specified period and optionally repeat.
  Extend, Retract, Timed Extend.
  isExtended – Check the state of the pneumatic cylinder.

## Slide 7: Exercise: 2-channel Pneumatic Cylinder
Control a 2-channel pneumatic cylinder to extend and retract using game controller buttons.
  Create and configure a game controller.
  Create and configure a 2-channel pneumatic object.
  Create a button event handler and hook it up to the game controller object.
  Add code to the button event handler to extend or retract the cylinder.
  Add code to display pneumatic status.

## Slide 8: PID Controlled Actuator
Create an instance of a PID Actuator.
TrcPidActuator – Constructor needs instance name, 1 or 2 physical motors, a lower limit switch, a PID controller, movement range and other optional parameters.
PID Actuator object properties:
  setPositionScale – make actuator works with real world units.
  getPosition – inquire the actuator position.
  setTarget – set and hold the actuator position using PID control.
  setPower – move the actuator at the specified power and optionally hold position.
  setPowerWithinPosRange – move actuator at specified power but applying PID control when it is close to lower or upper position limits.
  setManualOverride – overriding PID control.
  zeroCalibrate – perform Zero Calibration.

## Slide 9: Exercise: Elevator
Control an elevator using an analog joystick.
  Create and configure a game controller.
  Create and configure a PID control actuator object.
  Create a button event handler and hook it up to the game controller object.
  Add TeleOp code for zero calibration and manual override.
  Add TeleOp code to run the elevator up and down.
  Add code to display elevator status.