## Slide 1: Advanced Robotics Programming Class Lesson 6: Robot Indicators
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn different types of LED Indicators:
  12V single color LED connected to some sort of ON/OFF digital switch (e.g. Relay, FrcDigitalOutput, FrcPneumatic)
  12V RGB LED strip connected to 3 ON/OFF digital switches displaying 7 possible colors (e.g. 3 channels of FrcPneumatic).
  12V RGB LED strip connected to 3 motor controllers on 3 PWM channels displaying continuous spectrum of colors.
  5V Addressable LED strip connected to one PWM channel displaying different color patterns.
  5V Addressable LED strip connected to a REV Blinkin LED controller using one PWM channel.
  I2c RGB LED Matrix panel connected to the I2c bus (FrcI2cLEDPanel).

## Slide 3: LED Indicators
12V single color LED can be powered and controlled by many different components:
  Digital output channel: outputs 5V and usually does not have enough current to power LEDs, so it controls some sort of LED driver circuit.
  Relay channel: controls a relay (e.g. Spike) that controls 12V power source ON and OFF to the LED. Most common way to control the ring light of the vision subsystem.
  Pneumatic channel: each channel can power 12V or 24V pneumatic valve. Pretend the 12V LED is a 12V pneumatic valve.
  Motor controller via a PWM channel: can control the brightness of the LED.
12V RGB LED strips have 4 pins: 12V, R, G and B. They are usually common cathode LEDs. That means they can’t be powered by typical components and must use some sort of LED driver circuit.
  Can be controlled just like 12V single color LEDs except we have to use 3 channels instead of 1.
  REV Blinkin LED Driver: Easiest way to control 12V RGB LED strips. Connects to a PWM channel. Have 200 built-in blinking color patterns. Just set a pattern and be done.
Addressable RGB color LED strips. They have 3 pins: 5V, GND and DI on one end and 5V, GND and DO on the other end so they can be chained together. They can be controlled by:
  1 PWM channel: pixel color data is sent serially out to the LED strip.
  REV Blinkin LED Driver: If put into Addressable LED mode, it can support Addressable LED strips.
RGB LED Matrix Panel are smart panels. It’s connected and controlled via I2C bus.

## Slide 4: Controlling LEDs Using Simple Components
Digital Output (FrcDigitalOutput):
  Constructor: instance name, digital output channel number.
  Method: setState - set it to either true or false (i.e. ON or OFF).
Relay (Relay):
  Constructor: Relay channel number, direction.
  Method: set - Set the relay state to kOn or kOff.
Pneumatic (FrcPneumatic):
  Constructor: instance name, PCM module number, channel number.
  Method: setState - set it to either true or false (i.e. ON or OFF).
Motor Controller (Spark):
  Constructor: PWM channel number.
  Method: set - set a positive value from 0.0 to 1.0 to control the percentage brightness of the LED.

## Slide 5: Exercise 1: Control Ring Light with a Button
Control a camera ring light with a button on the joystick.
  Create and configure a game controller and hook a button event handler to it.
  Create and configure a Relay object.
  Add code to the button event handler to toggle the ring light ON and OFF with a single button.

## Slide 6: Controlling RGB LED Strips
REV Blinkin (FrcRevBlinkin) can control 12V RGB LED strips and 5V Addressable RGB LED strips. Must switch mode to support proper LED strip by pressing a button.
  Constructor: instance name, PWM channel number.
  Method: setPattern – specifies the one of the 200 built-in blinking patterns.
Addressable RGB LED Strip (FrcAddressableLED) can be controlled by a PWM channel.
  Constructor: instance name, number of LEDs, PWM channel number.
  Methods:
    reset – turn all LEDs on the strip OFF.
    setEnabled – enable/disable the LED strip.
    setPattern – set the colors of individual LEDs on the strip.

## Slide 7: Exercise 2: Control an RGB LED Strip with 3-channel Pneumatic
Control a 12V RGB LED strip with a single button on the joystick cycling from OFF to all 7 different colors.
  Create and configure a game controller and hook a button event handler to it.
  Create and configure a 3-channel FrcPneumatic object.
  Add code to the button event handler to use a single button toggling the colors of the LED strip.

## Slide 8: Exercise 3: Control an Addressable LED Strip
Control a 5V Addressable LED strip using a joystick button making a color pixel travel down the strip each time the button is pressed.
  Create and configure a game controller and hook a button event handler to it.
  Create and configure a FrcAddressableLED object.
  Add code to the button event handler so that the first pixel will light up to a certain color and on each press of the button, the light up pixel will travel down the strip.
  Add code to the button event handler so that another button is used to cycle the colors of the light up pixel.
  Extra credit: when the pixel reached the end of the strip, reverse the direction and make the pixel travel back to the beginning.

## Slide 9: RGB LED Matrix Panel
RGB LED Matrix Panel (FrcI2cLEDPanel) is controlled by Arduino that connects to the robot via I2C bus and therefore is a smart device.
  Constructor: instance name, I2C port, optional I2C address.
  Methods:
    setEnabled – enable/disable the LED Matrix Panel.
    setTextLine – set a line of text on the panel.
    clearTextLine – clear a line of text on the panel.
    clearAllTextLines – clear the entire panel.

## Slide 10: Exercise 4: Control an RGB LED Matrix Panel
Control an RGB LED matrix panel using 4 joystick buttons each of which displays a different text message on the panel.
  Create and configure a game controller and hook a button event handler to it.
  Create and configure a FrcI2cLEDAddressableLED object.
  Add code to the button event handler so that 4 different buttons will send 4 different messages to the LED panel. The text message will scroll left continuously.
  Extra credit: Add code to the button event handler so that pressing another button will cause the text message to reverse the scroll direction.