## Slide 1: Advanced Robotics Programming Class Lesson 7: Autonomous
Titan Robotics Club FRC492
Michael Tsang (Programming Mentor)

## Slide 2: Agenda
In this lesson, you will learn everything about Autonomous:
  What is an autonomous program?
  Steamworks Autonomous Analyzed
  Multi-tasking Explained
  State Machine
  Event
  Timer
  Robot Command Module
  Exercise: Timed Drive Autonomous
  Exercise: Steamworks Autonomous
  Task

## Slide 3: What is an Autonomous program?
Autonomous program consists of a sequence of tasks to be performed by the robot using various sensors as input and actuators as output without any human control.
The easiest way to design an autonomous program is to break down the task sequence into steps in English and then translate them into code.
Let’s look at the autonomous period of the 2017 FIRST Steamworks season. 2017 FIRST Robotics Competition STEAMWORKS Game Animation – YouTube
Three ways to score in autonomous:
  Cross the baseline (5 pts).
  Score fuel in the boiler (1 pt per fuel into the top goal and 1 pt per 3 fuels into the bottom goal).
  Deliver gear to the airship (60 pts per rotor turning).
Autonomous period is only 15 seconds long, so we need to pick our strategy on what we can accomplish.
Here is a video of how we did in autonomous in one of the matches. First Steamworks: Galileo Semifinal 1 Match 1 (World Championship - Houston) - YouTube

## Slide 4: Steamworks Autonomous Analyzed
First, we set our autonomous goals trying to maximize our score within the 15-second period:
  Cross the baseline.
  Deliver the gear to the airship.
  Run as far as we could to our gear loading station on the opponent side and stop.
Then, we layout the strategy in English:
  Park the robot either on the left or the right side.
  Move forward 85 inches crossing the baseline.
  Turn left or right approx. 60 degrees toward the airship.
  Use vision to align with target.
  Move forward until about 7 inches in front of the peg.
  Deploy the gear onto the peg.
  Backup 36 inches.
  Turn back facing the opponent side.
  Move forward about 320 inches into the neutral zone.
  Stop.

## Slide 5: Multi-tasking Explained
Because of the short 15-second autonomous period, we must try performing tasks that don’t depend on each other in parallel.
Example: You have a birthday party coming up and your mom wants you to finish your home work, do the laundry as well as baking your own pizza for the party. So you have three tasks (finish homework, do laundry, bake pizza).
Task 1: do laundry (total time – 2 hours)
  Put clothes into washing machine.
  Put in laundry detergent.
  Start washing machine.
  Wait for the washing machine to beep.
  Move the clothes into the dryer.
  Put in fabric softener sheet.
  Start dryer.
  Wait for the dryer to beep.
  Take clothes out, fold them and put away.
Task 2: bake pizza (total time – 0.5 hour)
  Wait until half hour before party start.
  Set oven to preheat to 450˚F.
  Wait for the oven to beep.
  Put the frozen pizza into the oven.
  Set timer for 20 minutes.
  Wait for the oven to beep.
  Take pizza out and cut into 8 pieces.
  Put on plates and serve guests.

## Slide 6: Multi-tasking Explained (continue)
To do all these tasks, one could do task 1 to its completion before starting task 2. After task 2 is completed then starts task 3. But it will be a waste of time and most of the time spent is waiting.
Multi-task is a better way. Note that there are steps in the task just simply waiting. Instead of staring at the washing machine or the oven waiting for it to beep, switch to the other tasks to make progress.
Combined tasks:
  Do task 1 steps 1-3.
  Step 4 is to wait for the washing machine to beep, switch to task 2 and check if you are about half an hour before the birthday party starts. If not, switch to task 3 to do your homework until you hear the washing machine beeps or it is about half an hour before the party starts.
  If the washing machine beeps, switch back to task 1, do steps 5-7. Then switch to task 2 and check if you are about half hour before the birthday party starts. If not, switch back to task 3 and continue doing your homework.
  When it’s about half hour before the party starts, switch back to task 2 and do step 2.
  Switch back to task 3 to continue doing your homework.
  When oven beeps, switch back to task 2 and do steps 4-5.
  Switch back to task 3 to continue doing your homework.
  When the dryer beeps, switch back to task 1 and do step 9.
  When done, switch back to task 3 to continue doing your homework. Homework is now done.
  Switch back to task 2 and wait for oven to beep, then finish steps 7-8.

## Slide 7: State Machine
TrcStateMachine implements a state machine that keeps track of the state of a task. A state represents the step the task is executing. When a task is waiting for a step to finish, the state machine is put into waiting mode so the robot can switch to other tasks.
Every time the robot switches tasks, it checks which task has finished waiting (i.e. ready to run) and will resume that task to make progress. By doing this, every task has a chance to make progress when other tasks are waiting.
TrcStateMachine<T> Constructor: instance name.
Methods:
  start – starts the state machine with the given state (enable state machine and set initial state to the given state).
  stop – terminates the state machine (disable state machine).
  getState – returns the current state the task is in (return null if state machine is not started).
  setState – set the state machine to the given state.
  isEnabled – check if the state machine is enabled (i.e. started).
  isReady – check if the state machine is waiting (i.e. not ready).
  isTimedout – check if the condition the state machine is waiting has timed out.
  addEvent – add an event to the list of things the state machine is waiting for.
  clearAllEvents – clear the event list.
  waitForEvents – put the state machine in waiting mode waiting for the events on the list; have option to wait for any one event or all events on the list.
  waitForSingleEvent – same as waitForEvents except there is just one event, not a list of events.
  checkReadyAndGetState – if state machine is waiting, it will check the event lists for any signaling event(s). If so, the state machine will move to the next state; then it returns the current state of the state machine.

## Slide 8: Event
Event is the main ingredient in multi-tasking. It is a flag indicating something has finished. Most components in the TRC library can signal an event if it takes time to perform something. State machine uses them to determine if a task should be resume.
Event has three states: cleared, signaled and canceled.
TrcEvent Constructor: instance name, optionally specifying the initial state.
Method:
  get – gets the event state
  signal – sets the event to signaled state
  clear – sets the event to cleared state
  cancel – sets the event to canceled state
  isSignaled – check if the event is in signaled state
  isCanceled – check if the event is in canceled state

## Slide 9: Timer
From time to time, the robot needs a timing mechanism, waiting for a given period of time to past.
TrcTimer Constructor: instance name.
Method:
  set – starts a timer expiring x seconds from now and signals an event or callback when done.
  getExpiredTimeInMsec – returns the expired timestamp in the unit of msec.
  isExpired – checks if the timer has expired.
  isActive – checks if the timer is actively counting down.
  isCanceled – checks if the timer has been canceled.
  cancel – cancels an active timer.

## Slide 10: Robot Command Module
Robot command module represents an autonomous program. It implements the TrcRobot.RobotCommand interface:
  cmdPeriodic – called periodic to run the autonomous program, most likely implements a state machine.
  isActive – checked if the autonomous program is still running.
  cancel – abort the autonomous program, usually contain code to cleanup.

## Slide 11: Exercise: Timed Drive Autonomous
Control the robot to drive forward or sideway for 10 seconds on selecting a choice on the autonomous choice menu.
  Create and configure 4 motors for a mecanum drive base.
  Create and configure a mecanum drive base.
  Create a Robot Command Module (new Java class).
  Write code in the robot command module to run a state machine running the robot base in a given direction for a given number of seconds. Stop the robot at the end of the run.
  Create and configure a choice menu with 4 direction choices: forward/backward/left/right.
  Create and configure two number fields on the Driver Station:
    Drive Time: allow the user to enter the number of seconds to drive the robot base.
    Drive Power: allow the user to enter the drive power in the range of 0.0 to 1.0.
  Add code in FrcAuto to read the choices entered and execute the action.

## Slide 12: Exercise: Steamworks Autonomous
Create an autonomous command module for FIRST Steamworks that does the following:
  Wait for 5 seconds.
  Go forward 6 feet.
  Turn right 60 degrees.
  Go forward 3 feet.
  Deploy the gear using pneumatics.
  Back up 3 feet.
  Turn back to face forward.
  Go forward 10 feet.
  Stop

## Slide 13: Task
Task is multi-tasking unit. It contains code to be run in a multi-tasking thread. You can register a task to be execute at a certain time by a certain thread.
In Titan Robotics Framework, there are many task types you can register:
  START_TASK – runs in the main robot thread before a robot mode starts.
  STOP_TASK – runs in the main robot thread before a robot mode stops.
  PREPERIODIC_TASK – runs in the main robot thread before runPeriodic method is called.
  POSTPERIODIC_TASK – runs in the main robot thread after runPeriodic method is called.
  PRECONTINUOUS_TASK – runs in the main robot thread before runContinuous method is called.
  POSTCONTINUOUS_TASK – runs in the main robot thread after runContinuous method is called.
  INPUT_TASK – runs in the input thread.
  OUTPUT_TASK – runs in the output thread.
  STANDALONE_TASK – runs in a standalone thread.

## Slide 14: Main Robot Thread
When the robot is powered up, the following sequence is executed in the main robot thread.
  Execute Robot.robotInit method to create/initialize robot hardware, set initial robot mode to DisabledMode.
  Execute Robot.robotStartMode method to initialize robot not specific to the robot mode.
  Execute TrcRobot.RobotMode.startMode method to initialize robot specific to the robot mode.
  Execute all registered START_TASK.
  Execute all registered PRECONTINUOUS_TASK.
  If periodic ready, execute all registered PREPERIODIC_TASK.
  Execute runContinuous method.
  If periodic ready, execute runPeriodic method.
  Execute all registered POSTCONTINUOUS_TASK.
  If periodic ready, execute all registered POSTPERIODIC_TASK.
  If robot is staying in the same mode, go back to step 5, otherwise transition to the next mode by going to next step.
  Execute all registered STOP_TASK.
  Execute TrcRobot.Robot.RobotMode.stopMode method to do cleanup specific to the previous robot mode.
  Execute Robot.robotStopMode method to do cleanup not specific to the robot mode.
  Go to step 2.

## Slide 15: Other Threads
Input Thread: All registered INPUT_TASKs run in the Input Thread. Generally deals with reading sensors and input states.
Output Thread: All registered OUTPUT_TASKs run in the Output Thread. Generally deals with any kind of actuators and status indicators.
Standalone Thread: Every registered STANDALONE_TASK has its own thread. Generally used for very high performance tasks that require high frequency execution and low latency.

## Slide 16: Task Manager
TrcTaskMgr manages tasks. It provides methods to create/register/unregister tasks of different task types.
TrcTaskMgr is a singleton that exists on first use: TrcTaskMgr.getInstance()
Once you obtain the taskMgr instance, it provides the following method to create a task object:
  createTaskObj – instance name of the task and the method that contains the code for the task.
The task object provides the following methods:
  registerTask – task type the task will be registered for. A task can register for multiple task types.
  unregisterTask – task type the task will be unregistered or to unregister all task types.
When a task is registered for a task type, its task method will be called at the appropriate time on the appropriate thread depending on the task type.

## Slide 17: Cautions on Multi-tasking
Since multi-tasking involves multiple threads (main robot thread, input thread, output thread and some number of standalone threads), care must be taken to understand problems introduced in this kind of environment which are derived from two main issues.
  Resource contention – shared access to data.
  Synchronization – coordination between different threads.
Resource contention: shared data between multiple threads can be easily corrupted seemingly randomly. Solution is controlled atomic access to shared data.
Synchronization: multiple threads can run with different speeds. When one thread’s execution depends on calculations from another thread, one must make sure these threads are synchronized so one thread will get the proper result from another thread at appropriate time. Solution is synchronization notifications.
Solutions to these problems sometimes create more problems: e.g. deadlock or performance issues. That’s why multi-tasking programming is really hard. Should avoid it if possible. If unavoidable, try minimizing the problems: limit data sharing and the need for synchronization.
Fortunately, Titan Robotics Framework provides some mechanisms that will help in some aspects of multi-tasking. For example, TrcEvent provides synchronization notifications between threads.